## Slide 1: CV1711 ENGINEERING DRAWING & 3D BUILD INFO MODEL (LAB)

## Slide 2
Instructor Information
NAME: CUI SHUAIWEN (SHAUN)
EMAIL: SHUAIWEN001@e.ntu.edu.sg
TEL: 83071903
Any questions? Feel free to reach out!

## Slide 3
WEEK 1 & 2 – CAD Basics
Learn AutoCAD basics on NTULearn
Submit E2 by the end of week 2
After that, move on to week 3, 4, …
Linkedin Video Access Issue?
Any questions? Feel free to reach out
Mark your attendance before leaving
Save files & sign out before leaving

## Slide 4
WEEK 3 – CAD Basics
Follow the instructions and videos on NTULearn
Submit E3 & E5 by the end of week 3
After that, move on to week 4 (orthographic projection), week 5 (auxiliary projection), week 6 … much more difficult, please preview the material before class.
Any questions? Feel free to reach out
Mark your attendance at the end of class
Save files & sign out before leaving

## Slide 5
WEEK 4 – Orthographic Projection
Let’s watch this youtube video for basic understandings.
https://youtu.be/heIobpUVZqc?si=No0iEweG8M1roWwM

## Slide 6
Quadrant System and Orthographic Projection
Third Angle Projection
First Angle Projection

## Slide 7
Quadrant System and Orthographic Projection
First Angle Projection
Third Angle Projection
The Projection is behind the object.
The Projection is in front of the object.

## Slide 8
First-angle projection:
T = elevation / front
S = end / side
P = plan / top
T
S1
P
Base
Unfold such that elevation view is adjacent to / center of other views.
First-angle projections are behind the object.
Vertical partition
Elevation
Plan
Horizontal partition
Vertical partition
Lid
S2
End 1
End 2
Base
Lid
Horizontal partition
Elevation is always on the vertical partition of the box.
Plan is always on the horizontal partition of the box.

## Slide 9
S
T
T
S
Comment:
Notice that P may not be given, because plan view is always from above.
Vertical partition
Base
Lid
Horizontal partition
Not required
First-angle projection:
Variation 1

## Slide 10
S
T
T
S
Vertical partition
Base
Lid
Horizontal partition
First-angle projection:
Comment:
The object is rotated.
Not required
Comment:
The layout stays the same because the object is simply rotated.
Variation 2

## Slide 11
S
T
T
Vertical partition
Base
Lid
Horizontal partition
First-angle projection:
Not required
S
Comment:
The other end view is requested.
Comment:
Take note that the layout is different now. Because first-angle projections are behind the object.
Take note of the hidden line.
Variation 3

## Slide 12
Vertical partition
Base
Lid
Horizontal partition
First-angle projection:
Not required
Comment:
The other end view is requested.
Comment:
Take note that the layout is different now. Because first-angle projections are behind the object.
Take note of the hidden line.
T
S
S
T
Variation 4

## Slide 13
Third-angle projection:
T = elevation / front
S = end / side
P = plan / top
T
S1
P
Base
Unfold such that elevation view is adjacent to / center of other views.
Third-angle projections are in between the object and the viewer / in front of the object.
Horizontal partition
Vertical partition
Lid
S2
Elevation is always on the vertical partition of the box.
Plan is always on the horizontal partition of the box.
Same as first-angle, even the locations of End 1 and End 2.
Vertical partition
Elevation
Plan
End 1
End 2
Base
Lid
Horizontal partition

## Slide 14
S
T
Comment:
Notice that P may not be given, because plan view is always from above.
S
Vertical partition
Base
Lid
Horizontal partition
Not required
T
Comment:
Remember, projections are in front of the object for the third angle.
Third-angle projection:
Variation 1

## Slide 15
S
T
S
Vertical partition
Base
Lid
Horizontal partition
Not required
T
Third-angle projection:
Comment:
The object is rotated.
Comment:
The layout stays the same because the object is simply rotated.
Variation 2

## Slide 16
S
T
Vertical partition
Base
Lid
Horizontal partition
Not required
T
Third-angle projection:
Comment:
The other end view is requested.
Comment:
Take note that the layout is different now. Third-angle projections are in front of the object.
Take note of the hidden line.
S
Variation 3

## Slide 17
S
T
S
Vertical partition
Base
Lid
Horizontal partition
Not required
T
Third-angle projection:
Comment:
The elevation view of the question has changed.
Comment:
The final drawings are the same as Variation 1.
Variation 4

## Slide 18
SCAN TO DOWNLOAD THE SLIDES

## Slide 19
WEEK 4 – Orthographic Projection
First Quadrant
Plan is always below elevation
Project the view at the back of project
Third Quadrant
Plan is always above elevation
Project the view in front of the object plane
Direction T
Elevation View (first to draw)
Direction S
End of View
Distance from Horizontal & Vertical Plan must be equal for projecting points, lines &surface measurements from one view to another views
https://www.youtube.com/watch?v=heIobpUVZqc

## Slide 20
WEEK 4 – Orthographic Projection

## Slide 21
WEEK 5 – Auxiliary Projection
Very Import, Please Pay Close Attention!

## Slide 22
Third Angle Projection
First Angle Projection
WEEK 5 – Auxiliary Projection – Recap

## Slide 23
WEEK 5 – Auxiliary Projection – Terms
First (Primary) Auxiliary Projection: A view projected onto a plane that is perpendicular to one principal view, used to show an inclined surface in its true size and shape.
First / Primary: The projection obtained by rotating once from a principal view (front, top, or side). Not First Quadrant.

## Slide 24
WEEK 5 – Auxiliary Projection – Auxiliary Plan
Some Kind of Plan:
– More Like Plan
– Perpendicular to Elevation View

## Slide 25
PLAN

## Slide 26
WEEK 5 – Auxiliary Projection – Auxiliary Elevation
Some Kind of Elevation:
– More Like Elevation
– Perpendicular to Plan View

## Slide 27
WEEK 5 – Auxiliary Projection

## Slide 28
WEEK 5 – Auxiliary Projection
First Quadrant (Angle)
Third Quadrant (Angle)
Auxiliary Plan
Auxiliary Elevation

## Slide 29
Example
- First Angle
- First Auxiliary Plan
Features:
- Projection behind the Object
- Perpendicular to Elevation View Projection

## Slide 30
Example
- First Angle
- First Auxiliary Elevation
Features:
- Projection behind the Object
- Perpendicular to Plan View Projection

## Slide 31
Example
- Third Angle
- First Auxiliary Plan
Features:
- Projection before the Object
- Perpendicular to Elevation View Projection

## Slide 32
Example
- Third Angle
- First Auxiliary Elevation
Features:
- Projection before the Object
- Perpendicular to Plan View Projection

## Slide 33
EXAMPLE 1

## Slide 34
EXAMPLE 1

## Slide 35
EXAMPLE 2

## Slide 36
EXAMPLE 2

## Slide 37
EXAMPLE 3

## Slide 38
EXAMPLE 3
hidden line missed!

## Slide 39
EXAMPLE 3

## Slide 40
SCAN TO DOWNLOAD THE SLIDES

## Slide 41
WEEK 6 - AUXILIARY PROJECTION

## Slide 42
AUXILIARY PROJECTION - PRECEDURES
1. Reproduce the principal views
2. Projectors parallel to the given direction from end points
3. Ground line perpendicular to the projectors
4. Transfer heights/widths

## Slide 43
AUXILIARY PROJECTION – CURVES APPROXIMATION
How many points ? Up to you
Rule of thumb

## Slide 44
AUXILIARY PROJECTION – FURTHEST POINTS

## Slide 45
AUXILIARY PROJECTION – EDGE OF COLUMNS

## Slide 46
AUXILIARY PROJECTION – HIDDEN LINES
CMD - Break

## Slide 47
AUXILIARY PROJECTION – HIDDEN LINES

## Slide 48
QUIZ
SEATING – Every Other Column
QUIZ PAPER (cannot be taken out) – Write down Name + Matr.No.
NO INTERNET CONNECTION, ONLY NTULearn Access
DWG + PDF – Learn how to export them

## Slide 49
SCAN TO DOWNLOAD THE SLIDES